## Slide 1
HackerzIOT
Deeksha Bestta 8106012911 (Leader)
IOT
IoT Home application using GSM-based celluler

## Slide 2: This research work investigates the potential of ‘Full Home Control’, which is the aim of the Home Automation Systems in near future. The analysis and implementation of the home automation technology using Global System for Mobile Communication (GSM) modem to control home appliances such as light, conditional system, and security system via Short Message Service (SMS) text messages is presented in this paper. The proposed research work is focused on functionality of the GSM protocol, which allows the user to control the target system away from residential using the frequency bandwidths. The concept of serial communication and AT-commands has been applied towards development of the smart GSM-based home automation system. Home owners will be able to receive feedback status of any home appliances under control whether switched on or off remotely from their mobile phones. PIC16F887 microcontroller with the integration of GSM provides the smart automated house system with the desired baud rate of 9600 bps. The proposed prototype of GSM based home automation system was implemented and tested with maximum of four loads and shows the accuracy of ≥98%.
ABSTRACT

## Slide 3: NOVELTY
The 8-bit PIC16F887 microcontroller generally consists of timers, Analog to Digital Converters (ADCs), and Universal Synchronous Asynchronous Receiver Transmitter (USART). In the proposed research work, the microcontroller receives instructions and decodes them to give device address and command, then sends corresponding signals to the driver of the power circuit. In addition, the microcontroller ensures dual independent operation action to turn on the device or switch it off. A feedback status of any devices under control whether switched on or off will be provided by the microcontroller. The RS-232 interface standard defines the electrical and mechanical details of the interface between Data Terminal Equipment (DTE) and Data Communications Equipment (DCE), which employ serial binary data interchange. The current version of the standard refers to DCE as Data Circuit terminating Equipment. Physically, interfacing between the PIC16F887 and GSM modem was implemented using RS232 standard installed on Max232. Since the system design has not included a battery, an external power supply is connected to the system to drive sufficient amount of current through the circuit connections. Relays had been connected to the output loads for a stable electrical control because these relays can provide feeding for different voltage level loads. Hence, the output selection becomes easier at any voltage. Fig. 2 demonstrates the simulation of the proposed GSM based home automation system being implemented in several stages. The PIC16F887 was simulated with the GSM modem by connecting it to the physical ports on the PC. MAX232 was placed to ensure proper transmission of data between the two terminals. Virtual terminal monitors the text sent from, and to the PIC16F887 while checking the transmission process and testing the algorithm. The waveform of the transmitted and received messages is monitored from the oscilloscope. While simulating the GSM modem, the “COMPIM” clock physically tests the response of the GSM modem by connecting it to a physical port on PC.

## Slide 4: TECHNOLOGY STACK
A layout is designed using Proteus ISIS Professional,
while adding Virtual Terminal and connecting it to COMPIM,
which is physically the DB9 connector in the PC terminal. It
can be added from the library .
The message alert text indicates that the message has been successfully
received and stored in the SIM card in the memory location.

## Slide 5: Hardware or software implementation
The design of our proposed smart GSM-based home
automation system. The architecture consists
of mobile phone and GSM modem. In the proposed system
design, incoming SMS message is sent from the user phone to
the GSM modem as a text message via cellular network. The
GSM modem then sends the commands in text mode to the
PIC microcontroller using an RS232 interface. The RS232
voltage levels are at ±12V whereas both the microcontroller
input and output operates at 0V to +5V. Since RS232 is not
compatible with microcontroller, MAX232 is utilized to
enable the communication between both the GSM modem and
PIC microcontroller by converting RS232 level signals to TTL
level signal. Outgoing message from the system containing the
home appliances status is delivered to the mobile phone
through GSM modem.

## Slide 6
BUSINESS SCOPE
The prototype of the proposed GSM based home
automation system. A 12V is supplied to the
voltage regulator to power the circuit. MAX232 is connected
to the GSM modem and the system run smoothly after the text
message was received. The output loads were activated and
automated the house in desirable basis.
Recently, the home automation market is very promising
field that is growing very fast and needs vast range of
developments that can be carried out in the concept of smart
home. In this project design and implementation of smart
GSM house was considered. PIC16F887 microcontroller with
the cooperation of GSM provides the smart automated house
system with the desired baud rate of 9600 bps. The proposed
prototype was implemented and tested with maximum of four
loads and shows the accuracy of ≥98%.